# Updates of Linear charger in Dec 2018
# Updates of Buck in Dec 2018
Criteria
- Catalog
  Power management >> Stepdown(Buck) >> Integrated switch(IC)
- Vin
  Vin_min ≤ 9
  Vin_max ≥ 20V
- Vout
  Vout_min ≤ 9
  Vout_max ≥ 9.5V
- Iout
  200mA ≤ Iout ≤ 3A
- Channels
  1
- Mode
- Efficiency
  η ≥ 90% @ 200mA
  η ≥ 80% @ 10mA
  η ≥ 50% @ 1mA
- Iq
  Iq ≤ 0.1mA
- Features
  Enable
  Light load efficiency
  Synchronous Rectification
  Current limiter: 200mA-500mA
- Package
- Price
  Price ≤ $1 @1000 pieces
Comparison

Part No.	Vin	Vout	Iout	η	Iq	I lim	Feature	Pkg	Price
TPS54061	√	√	√	√	√	√	√
TPS560430	√	√	√	×	√	×	√
TPS54202	√	√	√	√	√	×	√
TPS54202H	√	√	√	√	√	×	√
TPS56339	√	√	√	√	√	×	√
TPS54335-1A	√	√	√	×	×	×	√
TPS54334	√	√	√	×	×	×	√
TPS54336A	√	√	√	×	×	×	√
TPS54335A	√	√	√	×	×	×	√
TPS54335-2A	√	√	√	×	×	×	√
TPS54302	√	√	√	√√	√	×	√

# Schematics of control circuitry

PlanI

PlanII

BuckConceptral

# Simulation of control circuitry
- MarcPlan.asc
- MyPlan.asc
- BuckConceptral.asc
# Parameter calculation
PlanI

Reference: ResistanceCal.m
1. PlanII
- For 7.9-8.2 Schmitt
  ∆= ± Vbatt * R8 / (R8 + R9)
  = ± 8.05V * 186k / (10Meg + 186k)
  ≈ ± 0.15V
  ∆= ± Vbatt * R10 / R11
  = ± 6.25V *402k / 10Meg
  ≈ ±0.25V
- For Voltage divider
  Vref_u = R5 / (R4+R5) * Vbatt
        = 1.65Meg / (1.65Meg + 6.34Meg) * 8.05V
     ≈	1.65V
  Vref_l = R7 / (R6+R7) * Vbatt
        = 1.65Meg / (1.65Meg + 4.64Meg) * 6.25V
     ≈	1.65V
1. Buck
  TPS54061_Cal.ods
2. Linear Charger
        TPS54061_Cal.ods

# Test result
1. Functional test
  Situation: 20mA regular load, switch on/off @ ground line by N-FET,
  Schmitt @ 7.9V-8.2V: around 7.9V~8.15
  Schmitt @ 6.0V-6.5V: around 6.05V ~ 6.55V
  Alkaline charging: Yes, 100mA max
  Solar Panel charging: Yes, around 20mA
  Quiescent current:
2. Control Circuitry
1. PlanI
  Issue: Leakage current from drain to source of N-MOSFET is 1uA typically. It is even higher than the current of voltage divider.
2. PlanII
1. Schmitt trigger 7.9-8.2: 7.88~8.18V
2. Schmitt trigger 6.0-6.5: 6.07V~6.6V
3. Current: 8uA~16uA
Buck
1. Functional
  200mA shut down: 190mA~200mA
  enable: yes
  UVLO: n/a
  f_sw: 400kHz
  duty: around 50%
2. Vin & Vout
  Vin RMS: 16V
  Vin ripple: 100mV
3. Ripple
  Vout_ripple @ 100mA: 70mV
  Vout_ripple @ 10mA: 70mV
  Vout_ripple @ 1mA:
  Iout_ripple @ 100mA:
  Iout_ripple @ 10mA
  Iout_ripple @ 1mA:
4. Efficiency
  η @ 100mA: 8.94V*100mA/ 17.997V / 53.3mA = 93.2%
  η @ 10mA: 8.94V*10mA/17.997V/5.9mA = 84%
  η @ 1mA: 8.94V*1mA/17.997V/1.4mA = 35.7%
5. Transient load
  Light load (0A) > high load(170mA): 1200mV, 1ms
High load(170mA) > light load(0A): 600mV, 40ms
1. f-domain close loop response
2. short: 58mV
3. Thermal
4. Quiescent current (disabled): <22uA

Linear Charger
1. Functional
  Charging current: around 100mA
2. Efficiency
3. Over & Under charging
4. Thermal
  P-MOSFET:
5. Temperature of Battery
6. Quiescent current (no bat attached): 50uA max